## Slide 1
PROTOPULSE
From idea to a tested hardware prototype, with an AI that can use real machines
Proto (the AI) · Baker (board cell) · Mixer (test head)
Pitch v2, revised after murder-board round 1 · Delhi · 30 Sep 2026
Notes: Open with the company, not the machines. Protopulse builds the physical layer an AI needs to prototype hardware. Proto is the product; Baker and Mixer are the first two machines it drives. This version responds to Prateek's round-1 feedback: softer claims, Proto-first, Baker-first raise, full competition and cost analysis.

## Slide 2
MURDER BOARD · PRATEEK
What we changed after round 1
2
Protopulse · pitch v2
Feedback | What the deck now says
Pitch the moat (Proto), not two robots | Proto leads. Baker and Mixer are its first hands and eyes
Don't look like a desktop PCB mill | Baker is a prototyping cell. Slide 18 covers why mills struggled
Avoid 'replaces a fabrication order' | We complement fabs. Proto hands frozen designs to them
Two products on ₹10 lakh is aggressive | Phase 1 is Proto + Baker. Mixer is Baker's test head
'Design at night, board in the morning' | Measured targets: ≈1.4–2.4 h per board, ≈15–20 min hands-on
Competition and their pricing | 14 alternatives compared, with prices and sources (slides 17–19)
What does the machine cost, and does it pay back? | Build ₹1.45 lakh; price ₹3.49 lakh; pays back after 59 boards
Does it scale to 1,000 / 10,000 / 1 lakh boards? | Not for production, by design. Slide 16 shows where a fab wins
Notes: Show the investor we listened. Each row maps a round-1 comment to the slide that answers it.

## Slide 3
THE SHIFT
Software: idea to product in hours. Hardware: still weeks.
3
Protopulse · pitch v2
Software, 2026
$100M ARR
Lovable reached it 8 months after launch, selling to people who can't code
2.3M active users, 180,000 paying subscribers
$400M ARR by Feb 2026
Describe it, and a model builds, runs and fixes it
Hardware, 2026
7–20 days
for one assembled board from JLCPCB to an Indian desk, door to door
≈₹6,700 per assembled iteration, before parts
5+ separate tools and skills before a board works
The AI can draw the board but can't make it or test it
Sources: TechCrunch 23 Jul 2025; founded.com / ecosistemastartup (Feb 2026); zbotic.in India shipping guide; JLCPCB pricing; Protopulse model (Board Cost sheet).
Notes: Software has a closed loop: the model writes code, runs it and reads the error. That is why a commerce graduate can ship an app. In hardware the loop breaks at the physical world. A board takes 7 to 20 days to reach India, and nobody measures it for you.

## Slide 4
THE GAP
AI already designs hardware files. It stops there.
4
Protopulse · pitch v2
Flux
AI PCB design
$49M raised; 1M+ users
Quilter
AI PCB layout
$40M raised; $25M Series B, Oct 2025
Diode
AI PCB design
$11.4M Series A, a16z
Claude + Fusion
CAD connector
Official, May 2026
Claude + Blender
3D connector
Official, Apr 2026
Idea
Files
Board
Test
Learn
AI works here
Humans, tools and weeks
What's missing
Machines that take instructions from an agent, and instruments that send real signals back to it. The reasoning is there. What's missing is hands and eyes in the physical world.
Sources: SiliconANGLE 27 Feb 2026 (Flux); BusinessWire 7 Oct 2025 (Quilter); Fenwick (Diode); claude.com/connectors/autodesk-fusion; digitalproduction.com 30 Apr 2026 (Blender).
Notes: This is the proof that the AI part is real. Investors have put about $100M into AI that produces hardware files. Every one of these outputs a file. None of them owns a machine that makes the board or an instrument that tells the model whether the board works. That missing loop is Protopulse.

## Slide 5
WHY EASE GROWS THE MARKET
How people learn hardware, and where they give up
5
Protopulse · pitch v2
1
Idea → spec
What exactly should it do?
2
Parts
Datasheets, availability, footprints
3
Schematic
Circuit theory, reference designs
4
Layout
EDA tool, DRC, manufacturability
5
Fabrication
Gerbers, vendors, customs, 7–20 days
6
Assembly
SMD soldering, stencil, reflow
7
Bring-up
Scope, logic analyser, firmware
8
Iterate → volume
Debug root cause; DFM for a fab
Each rung needs new knowledge before you can climb it. Each one loses people.
People learn by doing: try, observe, adjust (Kolb's cycle). The speed of feedback sets the speed of learning.
2 weeks
per attempt: beginners give up, experts batch their changes
Same day
per attempt: a student gets many more tries in one semester
Notes: This is the learning-curve argument. Rungs 1 to 4 are knowledge that AI tools already help with. Rungs 5 to 8 need physical skills and equipment, and the feedback loop is weeks long. Every rung Proto removes brings in a new group of builders: students, product designers, domain experts. Lovable showed what happens to a market when the coding rung goes away.

## Slide 6
WHO WE ARE
We build smart prototyping machines and accessories for an AI, so going from idea to working prototype feels effortless.
Software team
Proto: the agent that plans, designs, runs the machines, reads the instruments and explains what happened
Hardware team
Baker and Mixer first. Later: 3D-printer integration and more smart accessories, all with an agent API
Manufacturing
China turnkey build. India does incoming test, minimal assembly and shipping: India first, then global
For prototyping, not production. Once a design is frozen, Proto hands the checked files to a fab.
Notes: This is the positioning Prateek asked for, in the founder's words. We are an engineering and product company. We don't want to become a factory, and we aren't a PCB-mill company.

## Slide 7
THE PRODUCT
Proto: one input in, a planned and tested prototype out
7
Protopulse · pitch v2
1. Input
Idea, sketch, photo, or KiCad / Flux / Fusion files
2. Plan
Spec, block diagram, parts in stock, test plan
3. Design
Schematic + layout via EDA connectors; Baker DRC
4. Make
Baker mills, masks, stencils and pastes the board
5. Assemble
Guided placement into a printed jig; reflow
6. Test
Mixer powers, drives and measures the board
7. Diagnose
Plain-language pass/fail and next change
8. Hand off
Checked Gerber/BOM/CPL to a fab for 100+ units
A person confirms before anything is cut, lasered or powered. Proto plans and checks; the machines only act on approved steps.
Notes: One input. Proto plans everything, can eventually operate the machines including a 3D printer, sets out the hardware and firmware, tests with real signals, flags problems and guides the user. The human is kept at safety gates and for part placement.

## Slide 8
TECH STACK · PROTO
Proto tech stack: an agent with real-world tools
8
Protopulse · pitch v2
Interface
Chat + sketch/photo upload · project timeline · Baker touch screen · browser
Reasoning
Frontier LLM, swappable, through an API · planner that breaks a goal into spec → parts → schematic → layout → fab plan → test plan
Tools (MCP)
KiCad scripting · Flux/KiCad import · Fusion & Blender connectors (enclosures) · parts APIs (stock, price) · ngspice · PlatformIO / arduino-cli
Machine drivers
Baker: Klipper + Moonraker API (motion, spindle, laser, UV, pumps, hotplate) · Mixer: FPGA over USB · resin/FDM printer driver
Verification
ERC/DRC · Baker-process DRC (V-bit trace/space, laser stencil aperture) · auto test plan from the netlist: expected rails, currents, signals
Data
Per-run log: design → process settings → measured result. This dataset is what no files-only AI tool has
Safety
Human approval gates · firmware interlocks (door, E-stop) · current limits on Mixer supplies · works offline for machine control
Runs on Baker's host (CB1 compute module in production) plus the cloud for the model. This is the target architecture; Phase 1 builds it for three reference designs.
Notes: Deep dive on the software. The moat is the data layer: every run logs what was designed, how it was made and what was measured. File-only AI tools can't collect that. The model is swappable, so we aren't tied to one vendor. MCP connectors are the same mechanism that already connects Claude to Fusion and Blender.

## Slide 9
MACHINE 1 · BAKER
Baker: a board-prototyping cell, not a desktop mill
9
Protopulse · pitch v2
Zone A · spindle + laser
01 Load · 02 Probe height map · 03 Mill + drill · 04 Vacuum clean · 10 Laser-cut stencil
Zone B · mask, UV, wipe
06 Coat mask · 07 UV image · 08 Wipe-develop + air knife · 09 Flood cure
Stencil + paste
05 Shuttle to Zone B · 11 Film clamp + paste · 12 Release, cut, return
Operator
13 Place parts with a vacuum pen into a printed jig · 14 Hotplate reflow
Mixer
15 One cable, eight instruments; Proto reads the results
Why it's different
One shuttle, one fixture, one coordinate frame from bare FR4 to paste
Stencil cut from the same Gerber in the same frame: no stencil alignment step
Placement jig prints while steps 01–12 run
Mask, stencil, paste and reflow in one box. A mill does none of these
Board: 100 × 160 mm copper-clad FR4, fed from a magazine onto two registration pins.
Notes: Fifteen steps, one shuttle. The shuttle is Baker's long X axis and runs under both zones, so the board never leaves its fixture until the parts go on. That registration is our process IP. It's what a stand-alone mill plus a separate stencil can't give you.

## Slide 10
TECH STACK · BAKER
Baker tech stack (1/2): motion, cutting, masking
10
Protopulse · pitch v2
Subsystem | Prototype build | Production direction | Why
Frame | 20×40 T-slot, 6 mm 6061 plate, 3 mm acrylic, orange 450 nm window | Sheet-metal frame + acrylic panels | Rigidity; laser-safe viewing
Motion X/Y | 3 ball-screw stages 200–300 mm, NEMA23 + DM556 | SFU1605 ball screws on HGR15 rails, NEMA23 1.26 Nm | ≈₹5,500 per axis instead of ₹16,500
Motion Z (×2) | 100 mm SFU1605 stage + NEMA17 | T8 screw + linear guide | Spindle/laser Z and dispense Z
Height map | Pogo-pin touch probe, grid probing | Same | FR4 isn't flat; cut depth follows the map
Spindle | 500 W ER11, 20° 0.1 mm V-bits, carbide drills 0.3–1.2 mm | Qualified volume spindle | Isolation milling + drilling
Laser | 10 W (9.5 W optical) 445 nm diode, air assist, fixed offset | Volume-sourced diode module | Cuts the polyimide stencil
Dust | 1000 W wet/dry vacuum | Integrated extraction | Keeps chips off the mask
Solder mask | Syringe-dispensed alkali-developing LPSM | Same, metered | Mask on clean, finished copper
UV imaging | 10.1 in 12K mono LCD + 405 nm parallel UV + ChiTu L K1 | Same engine also prints jigs | Cures everything except the pads
Develop | Dilute Na₂CO₃ wipe, peristaltic pump, squeegee, 5015 air knife | Same | No tank or bath; a few mL
Source: Protopus cost report and BOM, 29 Sep 2026. Production direction is from the China-parts production BOM.
Notes: Deep technical slide 1. Stress the design choices that make production cheaper: ball screws on rails instead of finished stages, and the same 10.1-inch UV engine for masking and, later, jig printing.

## Slide 11
TECH STACK · BAKER
Baker tech stack (2/2): stencil, placement, reflow, control
11
Protopulse · pitch v2
Subsystem | Prototype build | Production direction | Why
Stencil film | Polyimide roll; 4 × 12 V 8 kg electromagnets clamp a 430 steel frame; 25 N solenoid cut-off | Controlled film feed, align and cut | A fresh stencil for every board, already aligned
Paste | Sn42Bi58, melts at 138 °C; squeegee | Same | Cooler hotplate, less warp, jig-safe
Placement jig | Phrozen TR300 resin (HDT 160 °C) on Elegoo Saturn 3 Ultra 12K | Vat + lift on Baker's own UV engine | One pocket per part; removes the separate printer
Placement | Foot-pedal vacuum pen: 12 V pump + NC valve | Same | Cameras and feeders removed; ₹20,000 → ₹4,891
Reflow | 300 W silicone pad, SSR-25DA, MAX31855 + K-type, 5015 cool-down | Same, profiled | Low-temperature profile
Compute | Raspberry Pi 5 host + BTT Octopus Pro (Klipper), 7 in touch display | BTT CB1 + Manta M8P V2 (8 TMC2209), HDMI7 | ≈₹10,800; fewer boards
Power | Mean Well LRS-350-24, -350-48, -150-12 | One LRS-350-24 rail | Simpler harness
Safety | 2 × door interlock, E-stop, OD6+ goggles, 450 nm window | Class 1 enclosure goal | A 10 W laser is Class 4 if exposed
Firmware | Klipper + Moonraker; Proto job runner | Signed release binaries | Agent-controllable machine API
Source: Protopus cost report and BOM, 29 Sep 2026. Placement is manual by choice: it keeps cost down and a person in the loop.
Notes: Deep technical slide 2. Placement is deliberately manual with a printed jig: the jig does the aiming. That brought section F down from ₹20,000 to about ₹4,900, and it's the honest answer to 'it's not fully automated': it isn't meant to be.

## Slide 12
REPLACES 'DESIGN AT NIGHT, BOARD IN THE MORNING'
Honest cycle time: ≈2 hours, 15–20 minutes hands-on
12
Protopulse · pitch v2
Chart: Target minutes per step (100 × 160 mm, ~40 parts)
| Load + probe | Mill | Drill | Clean | Mask coat | UV image | Develop + dry | Flood cure | Laser stencil | Paste + release | Place (manual) | Reflow + cool | Test on Mixer
Low (min) | 5 | 25 | 5 | 2 | 3 | 2 | 4 | 5 | 5 | 3 | 7 | 10 | 5
High (min) | 5 | 45 | 10 | 2 | 5 | 4 | 6 | 10 | 10 | 3 | 14 | 12 | 15
81–141 min
per board, end to end
≈15–20 min
hands-on: load, place, hook up the test
3–5 boards
per 8-hour shift, one machine
These are engineering targets. Phase 1 measures them on real boards and reports the actual numbers.
Notes: Prateek was right that 'send it at night, pick it up in the morning' overclaims. You load boards and place parts. The honest claim: a board in about 1.4 to 2.4 hours, with 15 to 20 minutes of it hands-on. The jig prints in parallel, so it doesn't add time. Compare that with 7 to 20 days.

## Slide 13
ENGINEERING RISK, STATED OPENLY
What we still have to prove, and how we'll test it
13
Protopulse · pitch v2
Open point | How Phase 1 tests it | Fallback if it fails
Mask cleanliness on 0.5 mm-pitch pads | Wipe-develop test coupons under a microscope | Skim the pads with the spindle
Film registration within ±50 µm after magnetic clamping | Fiducial measurement on every coupon | Optical fiducial correction
Jig pocket accuracy after the resin shrinks | Measure pocket-to-pin on printed jigs | Scale compensation in the slicer
Laser offset drift with temperature | Check against a fiducial every job | Automatic re-offset routine
Double-sided boards | Flip on the same pins; measure layer-to-layer error | Single-sided + jumpers for v1
Rows 1–4 come from our own workflow document. Row 5 is added here so nobody finds it in diligence first.
Notes: Listing risks builds trust with a hardware investor. Each one has a test and a fallback, and Phase 1 money is allocated to them: ₹1.2 lakh in the use of funds.

## Slide 14
MACHINE 2 · MIXER
Mixer: the test head that lets an AI see
14
Protopulse · pitch v2
2-ch oscilloscope
2-ch waveform generator
16-ch logic analyser
Pattern generator
Protocol decoder
Programmable supply 1
Programmable supply 2
24-bit multimeter
One cable. Eight instruments.
It isn't trying to be a better scope than a Digilent. It's an instrument an agent can drive.
How Proto uses it
1
Reads the netlist and design intent
2
Sets the supplies with current limits; checks quiescent current
3
Checks each rail with the 24-bit meter
4
Drives inputs with the waveform/pattern generator
5
Captures scope and logic; decodes I²C/SPI/UART
6
Compares against what it expected; reports in plain words what failed and why
Notes: Mixer closes the loop. Test instruments today show waveforms to a person who has to interpret them. Mixer gives the numbers to Proto, which already knows what the circuit is supposed to do. It's also the production test fixture for Baker in the China factory, so one design does two jobs.

## Slide 15
TECH STACK · MIXER
Mixer tech stack: signal chain, prototype vs production
15
Protopulse · pitch v2
Probes / BNC
AD8066 buffers + relay ranges
ADC
FPGA + PSRAM
USB 2.0 HS
Proto
Block | Prototype (tune the analog first) | Production (≈₹13,740 landed)
FPGA | Sipeed Tang Primer 20K dock | Tang Nano 9K: GW1NR-9 + 64 Mb PSRAM
Scope ADC | 2 × AD9226, 12-bit 65 MS/s | AD9288 dual 8-bit 80 MS/s
Generator DAC | AN9767 dual 14-bit 125 MS/s | 2 × DAC908 8-bit 165 MS/s
Front end | 4 × AD8066 FET op-amps, REF5025, 8 range relays | Same op-amps and reference
Multimeter | ADS1256 24-bit | ADS1256 24-bit
Supplies | MCP4728 DAC setpoints, 2 × XL6009, 2 × INA226 monitors | Supply DACs, INA226, protection
Logic | 16 ch via 2 × 74LVC245 | 16 ch logic header
Host link | Raspberry Pi 5 + 7 in display | FT232HL USB 2.0 HS; no screen of its own
Board / case | 4-layer carrier PCB; vacuum-formed shell | 4-layer PCB assembled at JLCPCB; extruded aluminium
The production trade: 8-bit converters and no screen get it under ₹15,000. Digilent AD3 has 14-bit converters; we compete on price and on being driven by the agent, not on resolution.
Notes: Be upfront: production Mixer uses 8-bit converters, lower resolution than an Analog Discovery 3. It's a test head for pass/fail and debugging typical prototype boards, driven by an agent. The prototype keeps 12/14-bit parts so we can tune the analog front end first.

## Slide 16
PRATEEK: 1,000? 10,000? 1 LAKH?
Prototyping, not production: where a fab wins
16
Protopulse · pitch v2
Boards per year | Bakers needed* | Right tool | Why
10 | 1 | Baker | Same-day iteration; fab minimums and shipping dominate
100 | 1 | Baker | One machine covers a busy lab or startup
1,000 | 2 | Baker for iterations, fab for batches | Any run of >10 identical boards goes to a fab
10,000 | 14 | Fab / EMS | That's production. Proto exports the checked Gerber/BOM/CPL
1,00,000 | 134 | Fab / EMS | Not what Baker is for, and we don't claim it
Baker covers design iterations 1 to 10. For a frozen design, JLCPCB's $2-for-5 boards win on cost, and Proto sends them files that have already worked on a real board.
* One shift, slow-cycle target (750 boards per year per machine). Protopulse model, Throughput & Scale sheet.
Notes: This answers the scalability question directly. Baker isn't meant to scale to production. Our scale comes from the number of labs and teams, not boards per machine. Fabs are a partner and a future referral channel, not an enemy.

## Slide 17
MARKET MAP
Competition and their prices
17
Protopulse · pitch v2
Product | What it is | List price | ≈₹ at ₹88/$ | Gap vs Protopulse
LPKF ProtoMat S104 line | Pro in-house PCB | Quote-only; full line ≈$96k new (2019) | ≈₹84 lakh | Several machines, trained operator, no AI or test
Voltera NOVA | Printed electronics | $45,974 | ≈₹40 lakh | Ink on flexible substrates; research tool
Makera Carvera / Air | Desktop CNC | $5,799 / $2,699 | ₹5.1 / 2.4 lakh | Mills only: no mask, stencil, assembly, test
BotFactory Squink | Ink PCB + pick-and-place | $3,199–4,499 | ₹2.8–4.0 lakh | Conductive ink, not copper FR4
Neoden YY1 | Pick-and-place | <$3,000 | <₹2.6 lakh | Places parts only
JLCPCB → India | Fab service | $2 / 5 boards + $8 PCBA setup | ≈₹6,700 per iteration | 7–20 days + customs; no testing
Indian 24 h fab | Fab service | ₹3,000–8,000 / 5 boards | same | Bare boards; assembly and test separate
Analog Discovery 3 | USB instrument | $375–379 | ≈₹33,000 | Person reads the screen
ADALM2000 / Moku:Go | USB instrument | $237–262 / $599–799 | ₹21k / ₹53–70k | Same
Flux | AI PCB design | $15–49 per editor/month | ₹1.3–4.3k/mo | Output stops at files
Protopulse Baker + Mixer | AI prototyping cell | ₹3,49,000 + ₹24,999 (proposed, ex-GST) | ₹3.74 lakh | Board to tested board, driven by Proto
Sources on slide 30. USD at ₹88 to match the cost report. Prices exclude Indian import duty and GST, so real landed prices are higher.
Notes: Every competitor either does one step or stops at files. Prices are list prices before Indian duty and GST. Our bundle sits between a desktop CNC and a pro LPKF line, but covers the whole loop.

## Slide 18
PRATEEK: 'A ROUGH HISTORY'
Why desktop PCB machines struggled, and our answer
18
Protopulse · pitch v2
Othermill → Bantam Tools
Kickstarter 2013 ($300k+). Bought by Bre Pettis in 2017. PCB and CNC machines since dropped; the company now sells art machines
Voltera V-One
Ink PCB printer; out of stock at resellers. Voltera moved up to NOVA ($45,974) for flexible electronics
BotFactory
Squink at $3,199–4,499; SV2 is now price-on-request, a niche research tool
Nano Dimension DragonFly
Additive-electronics unit sold to Inspira in Apr 2026: $2M cash, up to $12.5M total
Lesson → our answer
They automated one step
Users still needed a fab, and debugged by hand
→ We cover mill → mask → stencil → paste → reflow → test
They fought $2 fab boards on cost per board
A price war they couldn't win
→ We compete on hours per loop, not rupees per board
They sold a tool to experts
Small market, steep learning curve
→ We sell an outcome to people who aren't experts yet
No software moat
Hardware copied, margins squeezed
→ Proto + run data is the moat; the machine is how it acts
Sources: Hackaday / Make (Othermill, Bantam); ToolGuyd (Bantam exit); Elektor, Aniwaa (V-One); TechCrunch (Squink); Evertiq 8 Apr 2026 (Nano Dimension).
Notes: Take the rough history head on. The companies failed for specific reasons, and each has an answer. We're not a better mill. We're the first product where the machine is how an AI acts.

## Slide 19
POSITIONING, BOTH WAYS
Where alternatives lose to us, and where they win
19
Protopulse · pitch v2
Alternative | We win on | They win on (we say so)
Fab services (JLCPCB, PCBWay, Indian fabs) | Hours not weeks; no customs; stencil and test included; tighter learning loop | Cost at quantity, multilayer, finish quality. We hand volume to them
Pro in-house lines (LPKF) | About 1/20th the price of a full line; one box; an agent runs it; no specialist operator | RF and multilayer capability, plating, decades of process
Desktop CNC (Carvera) | Mask, stencil, paste, reflow, test; board-specific AI | Metal and wood machining; a general-purpose tool
Ink printers (Voltera, BotFactory) | Real copper FR4 that solders like a fab board | Flexible and stretchable substrates
USB instruments (AD3, M2K, Moku) | Agent-driven test plan from the netlist; integrated supplies + 24-bit meter | Resolution and bandwidth (AD3: 14-bit)
AI design tools (Flux, Quilter, Diode) | Closed loop to a real, measured board; physical run data | Layout depth. We integrate with them rather than compete
Notes: Saying where competitors beat us is what makes the rest credible to an investor who knows hardware. AI design tools are partners: Proto can take a Flux or KiCad design and make it real.

## Slide 20
PRATEEK: 'HOW MUCH IS THIS MACHINE GOING TO COST?'
What the machine costs to build, and what we sell it for
20
Protopulse · pitch v2
Chart: Baker (₹)
| Prototype build (India) | Production unit (China parts, Delhi build) | Proposed price (ex-GST)
Baker | 373418 | 144842 | 349000
 | Baker | Mixer
Prototype build | ₹3,73,418 | ₹74,847
Production unit | ₹1,44,842 | ₹13,740
Proposed price | ₹3,49,000 | ₹24,999
Gross margin | 58.5% | 45.0%
Prototype includes 35% duty/courier on imports + 15% contingency
Production: 100-unit batch, China parts, Delhi assembly + QC (₹12,000)
China turnkey quotes are pending (RFQ at 5–5,000 units)
Source: Protopus cost report 29 Sep 2026 (81 of 96 lines from live listings). Prices are proposals to test in pilots.
Notes: The prototype costs ₹3.73 lakh because it's bought retail in India with duty and contingency. The production unit is ₹1.45 lakh: ball screws on rails, one controller board, one 24 V rail, China parts. At ₹3.49 lakh the gross margin is 58.5%, normal for low-volume lab equipment with support.

## Slide 21
PRATEEK: 'SAY X LAKH... DOES IT CANCEL MY COST?'
Does it pay for itself? After about 59 boards
21
Protopulse · pitch v2
₹334
Baker consumables per board
₹6,721
Same board from JLCPCB, landed in India
59
boards to recover ₹3.74 lakh
Baker price (ex-GST) | Gross margin | Boards to break even vs JLCPCB | Startup, 2 boards/wk | Lab, 1 board/wk
₹2,99,000 | 51.6% | 51 | 6.4 months | 12.8 months
₹3,49,000 (proposed) | 58.5% | 59 | 7.4 months | 14.8 months
₹3,99,000 | 63.7% | 67 | 8.4 months | 16.8 months
Direct cash only. Waiting time (7–20 days per loop) and engineer hours aren't counted, and they're the bigger saving
Against an Indian 24-hour fab (bare boards only): 73 boards
Components are excluded on both sides: you buy the parts either way
Notes: This is Prateek's X-lakh question. On direct cost alone, Baker plus Mixer pays back after 59 board iterations against ordering from JLCPCB. A hardware startup iterating twice a week gets there in about 7 months. The workbook lets him change the price and usage and see it recalculate.

## Slide 22
BOTTOM-UP SIZING
Market: start in India's labs, then go global
22
Protopulse · pitch v2
5,868
AICTE-approved engineering colleges
23.2 lakh
B.Tech students enrolled
10,000
Atal Tinkering Labs set up, +50,000 over 5 years
2.25 lakh
DPIIT-recognised startups
India hardware pool (upper bound)
Colleges: 5,868 × ₹3.74 lakh
₹219.5 Cr
Startups: 1% of 2.25 lakh × ₹3.74 lakh
₹84.1 Cr
One-time hardware
₹303.6 Cr
Proto subscriptions / year
₹48.7 Cr
Global, after India
2,300+ Fab Labs in 120+ countries
Oscilloscopes: ≈$2.6–2.9B market in 2025
Smart desktop CNC mills: $1.0B (2024) → $1.4B (2031)
Sources: AICTE, AISHE, AIM/PIB, Budget 2025-26, DPIIT, Fab Foundation, Fortune BI, QYResearch (slide 30). 1% startup share is our assumption.
Notes: Bottom-up rather than a big analyst number. If every AICTE college bought one bundle, that's ₹220 crore of hardware; hardware-relevant startups add ₹84 crore. Institutions have grant budgets: ATLs get ₹20 lakh each, AICTE IDEA Labs about ₹1.1 crore. We start with colleges and startups, then Fab Labs abroad.

## Slide 23
HOW WE MAKE MONEY
Business model: machine once, Proto every year
23
Protopulse · pitch v2
Hardware
Baker ₹3,49,000 · Mixer ₹24,999 (ex-GST)
58.5% / 45.0% gross margin
Proto subscription
₹4,999/month per lab after year 1 (year 1 free)
Software margin; cloud cost to be measured
Consumable kits
₹699 per board: FR4, mask, paste, film, jig resin
Cost ₹334 → 52% margin
Fab hand-off (later)
Checked files sent to partner fabs for 100+ units
Referral revenue; no inventory
Per installed Baker, per year after year 1
₹1,64,838
recurring revenue
₹1,14,810
gross profit, at 150 boards a year
All prices are proposals that the Phase 1 pilots will test. Usage of 150 boards per year (about 3 a week) is an assumption.
Notes: The machine opens the account. Proto and consumables bring recurring revenue: about ₹1.65 lakh a year per installed Baker at 3 boards a week, roughly half the machine price every year.

## Slide 24
OPERATIONS
Manufacturing: China turnkey, India test and ship
24
Protopulse · pitch v2
China: parts, PCBA, frame, assembly
China: firmware, Mixer-based test, pack
India: incoming QC + minimal assembly
India: final test + serial number
Ship: India first, then global
Gate | Units | Exit criterion
DFM / RFQ | – | Technical + commercial shortlist
EVT-1 / EVT-2 | 5–20 / 10–30 | Repeatable build; critical issues closed
DVT | 20–100 | Design frozen
PVT | 100–500 | Signed production authorisation
Mass production | Volume | 100% functional test
RFQ shortlist (to qualify, not endorsements)
Primary: PCBWay, Seeed Fusion, Peakingtech, Shenzhen MHC
Scale option: Kaifa. Secondary: Grandtop, PCBONLINE, Shenze
We keep: test system, firmware releases, ECN/AVL approval, final acceptance
Contracts: NNN, tooling ownership, no overrun, no silent substitutions
Source: Protopulse Baker China manufacturing package (29 Sep 2026). RFQ quantities 5 / 10 / 25 / 50 / 100 / 250 / 500 / 1,000 / 5,000.
Notes: We stay an engineering company. The factory builds, tests on our Mixer-based fixture and packs. India does incoming QC, the few minimal assembly steps and final test, then ships: India first, then global. This starts only after Phase 1 proves the process.

## Slide 25
PRATEEK: 'START WITH BAKER FIRST?' WE AGREE.
Step by step: Proto + Baker first
25
Protopulse · pitch v2
Phase 1 · now · ₹10 lakh
0–9 months
Proto alpha: 3 reference designs from prompt to tested board
Baker prototype: full 15-step flow
Mixer built as Baker's test head, not launched on its own
Close the 4 open points with data
3 pilot sites, 50 boards, measured cycle time
Exit test
Prompt → tested board on 3 designs; 4 open points closed
Phase 2 · seed
9–18 months
EVT/DVT units through a China partner (5–30)
First paid customers: colleges + startups
Mixer launched commercially
Proto subscriptions start
Exit test
10+ paid units; EVT/DVT passed at a China partner
Phase 3 · scale
18–36 months
PVT and 100-unit batch
3D printer and more accessories under Proto
Fab hand-off partnerships
First markets outside India
Exit test
PVT yield signed off; 100 units shipped
Notes: We take the step-by-step advice. The ₹10 lakh round funds one thing: Proto driving Baker. Mixer is in it only because a board isn't done until it's tested, and it's only 17% of the hardware budget. Each phase has an exit test before we raise the next.

## Slide 26
PHASE 1 BUDGET
Use of the ₹10 lakh
26
Protopulse · pitch v2
Chart: 
| Baker prototype | Process validation | Proto software | Safety + IP | Reserve | Workshop tools | Pilot programme | Mixer (test head)
₹ | 373418 | 120000 | 100000 | 90000 | 86735 | 80000 | 75000 | 74847
Milestones the money buys
M3: Baker assembled; Zone A mills and drills
M5: first board through all 15 steps
M6: 4 open points closed with data
M7: Proto takes a prompt to a tested board on 3 reference designs
M9: 3 pilot sites, 50 boards, measured cycle time, letters of intent
45%
of the raise buys the two prototypes, costed line by line (₹4,48,265)
Total ₹10,00,000. Hardware lines from the 29 Sep cost report; other lines are plan allocations. Founder salaries not included.
Notes: Half the money goes to the two prototypes, which are costed line by line. The rest goes to proving the process, building the Proto alpha, safety and IP, and three pilots. Every milestone is measurable.

## Slide 27
DEFENSIBILITY
The moat is the loop, not the machine
27
Protopulse · pitch v2
Closed-loop run data
Every run links design → process settings → measured result. File-only AI tools can't collect it
Agent-native machines
Baker and Mixer expose state, calibration and actions to Proto. Other machines were built for a person at a keyboard
Process IP
One frame for mill, mask and stencil from the same Gerber: registration a stand-alone mill doesn't have
Cost base
₹1.45 lakh production Baker; China turnkey build with India test
Recurring revenue
Proto subscription + consumables ≈ ₹1.65 lakh per machine per year
Notes: Prateek said the strongest moat is hidden in the idea. It is: an agent that learns from real, measured builds. The machines are how we collect that data and how the agent acts.

## Slide 28
RISKS
Business risks and how we reduce them
28
Protopulse · pitch v2
Risk | How we reduce it
Process doesn't reach 0.5 mm pitch or ±50 µm | Phase 1 gates on coupons; fallbacks on slide 13; launch spec set by measured results
Laser and chemical safety in labs | Interlocked Class 1 enclosure goal, E-stop, a few mL of dilute Na₂CO₃ only, safety review in the budget
Colleges buy slowly | Price fits under grant budgets (ATL ₹10 lakh setup, IDEA Lab ≈₹1.1 Cr); startups as the faster second segment
Model and API costs | Model-agnostic; measure cloud cost per lab in pilots before fixing subscription price
Copycat hardware | Value is in Proto and the run data; the hardware is cheap to us by design
China supplier risk / IP | Two-supplier strategy, NNN, tooling ownership, we own the test system
Notes: Close the risk discussion before the investor opens it.

## Slide 29
THE ASK
₹10 lakh to prove that an AI can take a prompt to a tested board on Baker
9 months
to Phase 1 exit
3 + 50
pilot sites + boards
59
boards to customer payback
58.5%
Baker gross margin
Proto is the company. Baker is its first machine. Mixer is how it sees.
Protopulse · Delhi
Notes: End on the ask, the exit test and one line to remember.

## Slide 30
APPENDIX
Sources
30
Protopulse · pitch v2
Protopus cost report, BOM and Baker workflow story (29 Sep 2026); Baker China manufacturing package (29 Sep 2026)
JLCPCB pricing: jlcpcb.com PCB and PCBA pages; India shipping, duty and timing: zbotic.in guides
Indian fabs: zbotic.in rush-prototyping guide (PCB Power, Lion Circuits)
Voltera NOVA: store.voltera.io; V-One: eleshop.eu, elektor.com, aniwaa.com
Makera Carvera: PR Newswire via Utusan Malaysia (Jun 2026)
Bantam Tools: makezine.com, hackaday.com, toolguyd.com ('no longer sells CNC milling or PCB machines')
BotFactory: techcrunch.com, technical.ly; Nano Dimension AME sale: evertiq.com (8 Apr 2026), tctmagazine.com
LPKF: lpkf.com (quote-only); exapro.com used S104 line listing (~$96,000 new in 2019)
Neoden YY1: eevblog.com forum; Analog Discovery 3: jameco.com, digikey.com; ADALM2000: richardsonrfpd.com, Mouser
Moku:Go: tequipment.net; Red Pitaya: redpitaya.com; Saleae: saleae.com; Rigol DHO804: electro-meters.com
Flux: flux.ai pricing, siliconangle.com (27 Feb 2026); Quilter: businesswire.com (7 Oct 2025); Diode: fenwick.com
Claude connectors: claude.com/connectors/autodesk-fusion; digitalproduction.com (30 Apr 2026, Blender)
Lovable: techcrunch.com (23 Jul 2025), founded.com (Feb 2026)
India: AIM/PIB (10,000 ATLs), Union Budget 2025-26 (50,000 ATLs), AIM grant guideline (₹20 lakh), AICTE via educationforallinindia (5,868), AISHE (23.2 lakh B.Tech), TiE/DPIIT (2.25 lakh startups), MeitY/PIB (C2S), AICTE IDEA Lab EOI
Global: Fab Foundation (2,300+ labs), Fortune Business Insights (oscilloscopes), QYResearch via electronicsforu (desktop CNC)