## Slide 1
Focus on
innovation.
We take care of the rest.
proto, our AI engineer, plans every step.
baker makes the board. mixer tests it.
protopus-kappa.vercel.app
Notes: Proto now leads the line: the AI engineer is the company; Baker and Mixer are the machines it works through (Prateek, round 1).

## Slide 2
01 · EXECUTIVE SUMMARY
A prototyping lab and a full test bench,
on one desk, run by an AI engineer
MORNING
You describe it
Proto reads the design, checks it and points at what will bite later.
MIDDAY
Baker builds it
Milled, masked, stencilled and pasted. You drop parts into a printed jig; Baker reflows.
AFTERNOON
Mixer tests it
One cable, eight instruments, and a verdict Proto writes in plain words.
EVENING
You try again
The next attempt starts the same evening, not two weeks from now.
WHAT MAKES
IT OURS
Making and testing on one desk, with Proto guiding every step instead of a hundred buttons.
Built for prototypes: the first 1–10 boards of a design. Volume goes to a fab, with files that already worked.
Notes: Two wording changes from round 1: not 'a small electronics factory' (we are for prototypes), and placement is honest: you drop parts into a printed jig. Baker's own cycle is about two hours, so morning → evening holds.

## Slide 3
02 · PROBLEM
A prototype is a loop,
and every lap costs weeks
design
order
wait 2 weeks
solder by hand
test
bug found
AND AGAIN
×3, ×4, ×5
2
weeks waiting for a board to come back from a fabrication house
5
instruments to buy before you can even measure it
5
vendor apps and driver stacks to learn and keep alive
In my department a board ordered in week one gets measured in week four. Nobody is short of ideas. They are short of tries.
WHY NOW · compute is cheap enough for machines to carry the fidelity. People should carry the innovation.

## Slide 4
03 · WHY NOW
AI can already build the software.
Hardware is where it gets stuck.
SOFTWARE HAS A CLOSED LOOP
$100M ARR
Lovable, 8 months after launch, selling to people who can't code. The model writes the code, runs it, reads the error and fixes it.
AI ALREADY DRAWS HARDWARE
Flux
$49M raised · 1M+ users
Quilter
$40M raised · AI layout
Diode
$11.4M Series A · a16z
Claude ↔ Fusion, Blender
official connectors, 2026
…AND STOPS AT THE FILE
No model can make the board, power it, or see whether it works. The loop breaks at the bench, and a person carries it for two weeks.
idea
files
board
test
verdict
AI works here today
protopus gives the AI hands and eyes here
Smart machines + smart accessories = the AI's access to the real world.
TechCrunch 23 Jul 2025 · SiliconANGLE 27 Feb 2026 · BusinessWire 7 Oct 2025 · Fenwick · claude.com/connectors · digitalproduction.com 30 Apr 2026
Notes: The AI part is proven: about $100M has gone into AI that produces hardware files. All of it stops at the file. Protopus builds the machines and accessories that let a model make, measure and learn.

## Slide 5
04 · WHO WE UNLOCK
Every rung of hardware knowledge
loses people. Proto removes rungs.
RUNG
YOU USED TO NEED
WHO CARRIES IT NOW
01
idea → spec
What exactly should it do?
Proto asks, then writes it
02
parts
Datasheets, stock, footprints
Proto picks in-stock parts
03
schematic
Circuit theory, references
Flux + Proto check it
04
layout
An EDA tool, DRC
Proto fixes it (Baker Studio)
05
fabrication
Vendors, customs, 7–20 days
Baker, same day
06
assembly
SMD soldering, stencil, reflow
Baker + printed jig
07
bring-up
Scope, logic analyser, firmware
Mixer measures
08
debug
Root cause, next revision
Proto explains the fix
HOW PEOPLE LEARN
By doing: try, look, adjust (Kolb's cycle). The speed of feedback sets the speed of learning.
2 weeks
per try: beginners quit, experts batch changes
same evening
per try: a student gets many more attempts in one semester
Every rung we take away brings in a new crowd: students, designers, domain experts. Lovable showed what happens when the coding rung disappears.

## Slide 6
05 · SOLUTION
One AI engineer, and the two smart machines it runs
proto
A platypus AI engineer inside both machines.
Reads the design · plans the job · flags mistakes · explains results
baker
Makes the board, ready for parts.
Mill · drill · mask · laser stencil · paste · guided placement · reflow
mixer
Tests the board in real life.
Eight instruments behind one cable
VISION · a bridge between idea and innovation for anyone who wants to bring theirs to the world.
DEMO 1
Website walk-through · protopus-kappa.vercel.app
DEMO 2
Video · raw Baker prototype running
Notes: Proto first. Baker now reads 'guided placement', not 'pick and place': the operator drops parts into a printed jig, which is what the prototype does.

## Slide 7
06 · WHAT MAKES IT OURS
Proto: an AI engineer that understands your board
PROTOPUS Baker Studio
Proto has already found the thin trace, fixed it and planned the mill. You press Accept.
01
READS THE BOARD
Understands schematics and layouts. Pulls designs in through the Flux.ai API.
02
MAKES IT
Generates the Gerbers and the Baker job: mill, drill, mask, stencil, placement.
03
DIAGNOSES IT
Tests through Mixer, understands the waveforms and says in plain words what is wrong.
04
HAS A CHARACTER
A platypus engineer with a personality developed through Gemini.
COMING NEXT
Probe matrix accessory
A grid of probes under the board gives Proto full access to every net on the PCB: it can measure anything, not just what you clip.
Simple enough that a high-school student can print a board.

## Slide 8
07 · PROTO · HOW THE AI WORKS
Proto is a loop, not a chatbot: understand,
plan, check, make, measure, explain
YOU GIVE IT
an idea in words
a sketch or photo
Flux / KiCad files
a Gerber set
“why is this hot?”
UNDERSTAND
Parses netlist, footprints, stack-up into a board model
PLAN
LLM planner turns the goal into steps; asks when unsure
CHECK
DRC + Baker rules: trace, clearance, aperture, drill
MAKE
CAM engine: toolpaths, mask image, stencil, jig → Baker job
EXPLAIN
Compares measured vs expected; writes the verdict and the fix
MEASURE
Mixer runs the test plan: rails, currents, waveforms, buses
APPROVE
You press Accept. Nothing is cut, lasered or powered before
next attempt
YOU GET
a tested board and a sentence: what passed, what failed, where to look
MEMORY
Every run is logged: design → process settings → measurements → outcome. The next board, and every other Baker, learns from it. No files-only AI tool can collect this data: it is the moat.
Model-agnostic: the character runs on Gemini today; the planner calls any frontier model through an API. Machine control stays local and works offline.
Notes: How the AI actually works. The language model understands, plans and explains. Precise work (DRC maths, toolpaths, G-code, pass/fail limits) is done by deterministic engines Proto calls as tools. A person approves before anything physical happens. Every run feeds a memory that no files-only AI can build.

## Slide 9
08 · PROTO · ONE RUN, STEP BY STEP
What happens between “import” and “PASS”
baker studio — sensor-hat-rev-c.brd · 62.0 × 40.5 mm
10:02
you
import sensor-hat-rev-c from Flux
10:02
proto
DRC 0/0. Baker rules: one trace under the MCU necks to 5.8 mil.
10:03
proto
widened it to 7 mil and kept clearance. Board still fits. [Accept]
10:03
proto
job: isolation mill, 0.4 mm V, 2 passes · drill 42 holes · mask · stencil · jig
10:04
baker
steps 01–12 running · placement jig printing in parallel
11:40
you
drop parts into the jig pockets · vacuum pen
11:52
baker
reflow, Sn42Bi58 low-temperature profile
12:05
mixer
T2 power up: current limit set · idle current in range ✓
12:06
mixer
T3 rails: 3V3 within limit ✓
12:07
mixer
T6 I²C scan: no ACK from the sensor ✗
12:08
proto
“SDA has no pull-up. R4 is lifted on one pad. Reheat R4 and retest.”
12:15
mixer
retest: sensor ACKs, reading plausible ✓ PASS
WHAT PROTO CALLED
Flux.ai API
design in
DRC + Baker rules
found 5.8 mil
CAM engine
toolpaths, mask, stencil, jig
Klipper / Moonraker
ran Baker
Test-plan builder
from the netlist
Mixer driver
supplies, DMM, logic
Language model
the plain-words verdict
Illustrative run on the board shown in Baker Studio. Times are the engineering targets (≈2 h Baker cycle, ≈15–20 min hands-on); the proof of concept measures them.
Notes: A concrete run, from import to PASS. Proto calls tools; it doesn't improvise G-code. The diagnosis is where the language model shines: it links a missing I²C ACK to a lifted pull-up resistor and says what to do.

## Slide 10
09 · PROTO · GUARDRAILS AND ROADMAP
Where the AI is, and where it isn't
THE MODEL DOES
— understands what you want
— reads the design and datasheets
— plans the job and asks questions
— drafts the test plan
— explains results and proposes the fix
— has a character (Gemini)
THE ENGINES DO
— DRC maths and Baker process rules
— toolpaths, G-code, mask and stencil images
— jig geometry and placement map
— test limits and pass/fail
— current limits on every supply
— interlocks: door, E-stop, laser cut-off
YOU DO
— describe the idea
— press Accept before anything physical
— drop parts into the jig
— decide on the fix
— own the design and the IP
The model never drives a motor directly. It proposes; tested engines compute; you approve; the machine executes.
V0 · TODAY
Baker Studio: DRC fix + mill planning, with Proto inside
V1 · PROOF OF CONCEPT
Full Baker job + Mixer test plan + plain-words verdict
V2 · AFTER SEED
Idea → design via Flux/KiCad; enclosures via Fusion/Blender; 3D printer
V3 · FLEET
Learns from every Baker's run data; probe matrix sees every net
Notes: This slide answers 'is the AI safe near a spindle and a Class 4 laser?' and 'what is real today?'. V0 is running in Baker Studio; V1 is what the ₹16 lakh proves.

## Slide 11
10 · BAKER · AT A GLANCE
Fifteen steps on one shuttle, in one box
BAKER ENCLOSURE · T-slot frame · acrylic · 450 nm laser-safe window · door interlocks · E-stop
Kapton stencil film roll · 4 electromagnet clamp · solenoid cut-off
ZONE A · cross axis + Z
Spindle 500 W ER11
touch probe · V-bit · drills
Laser 10 W 445 nm
fixed offset · air assist
vacuum dust extraction
ZONE B · cross axis + Z
Mask: syringe LPSM
UV: 10.1" 12K LCD, 405 nm
Wipe: Na₂CO₃ + air knife
paste squeegee rides here too
FR4
mag
azine
⟷ SHUTTLE = long X axis · ball screw + NEMA23 · FR4 on 2 registration pins · runs under both zones
steps 01–12 happen in one coordinate frame
PLACE + REFLOW
steps 13–14
printed jig on
the same pins
vacuum pen
300 W hotplate
Sn42Bi58, 138 °C
MIXER
step 15
one cable
8 instruments
Proto reads
the results
resin printer, in parallel: prints the TR300 jig during steps 01–12
15
steps, blank FR4 → tested board
1
shuttle, one coordinate frame
100×160
mm board in the workflow
8
instruments on Mixer
Notes: The whole machine on one slide, from the workflow story. The shuttle never lifts or re-registers the board between cutting, masking and stencilling: that is the process IP.

## Slide 12
11 · BAKER · THE STORY OF ONE BOARD
From a plain sheet to a board ready for Mixer
STEPS 01 · 05
It starts as a plain sheet
FR4 drops from the magazine onto two registration pins. One coordinate frame from here to placement.
cast · FR4 blanks · dowel pins · ball-screw shuttle + NEMA23
STEPS 02–04
Zone A reads the board, then cuts it
A touch probe maps height on a grid, so the 0.1 mm V-bit cuts the same few microns everywhere. Same spindle drills; vacuum pulls the dust.
cast · pogo probe · 500 W ER11 · 20° V-bits · 0.3–1.2 mm drills
STEPS 06–09
Zone B finishes the copper
Liquid mask, a 10.1" LCD cures all but the pads, a dilute Na₂CO₃ wipe lifts the pads clean, air knife, flood cure. No tank, no bath.
cast · syringe LPSM · 12K mono LCD · 405 nm UV · peristaltic pump
STEPS 10–12
The stencil fits this exact board
The laser cuts pad openings in film above the board, from the same Gerber in the same frame. Magnets clamp, squeegee pastes, film is cut away.
cast · 10 W 445 nm laser · Kapton roll · 4 × 8 kg magnets · 25 N solenoid
STEPS 13
The jig does the aiming
While 01–12 ran, the resin printer made a jig with one pocket per part. You drop each part in with the foot-pedal vacuum pen.
cast · TR300 resin (160 °C) · vacuum pump + NC valve · foot pedal
STEPS 14 → 15
Reflow at low temperature
The jig lifts off; the hotplate runs a Sn42Bi58 profile (138 °C), below the resin's limit, with less warp. Then Mixer tests it.
cast · 300 W silicone pad · SSR-25DA · MAX31855 + K-type
Source: PROTOPUS Baker + Mixer workflow, “The story of a PCB” (29 Sep 2026).

## Slide 13
12 · BAKER · TECH STACK, PROTOTYPE → PRODUCTION
Same story, cheaper parts: ₹3,73,418 → ₹1,44,842
FUNCTION | PROTOTYPE (INDIA, 1 UNIT) | PRODUCTION (CHINA PARTS, 100) | WHY
Axes | Finished ball-screw linear stages | SFU1605 ball screws + HGR15 rails built in | ≈₹5,500 per axis vs ₹16,500
Z axes | 100 mm SFU1605 stage + NEMA17 ×2 | T8 screw + linear guide | Spindle/laser Z and dispense Z
Control | Raspberry Pi 5 + BTT Octopus Pro + DM556 | BTT Manta M8P V2 + CB1 (8 × TMC2209) | One board, 8 drivers, ≈₹10,800
Power | 24 V + 48 V + 12 V supplies | One LRS-350-24 rail (spindle keeps its own) | Fewer supplies, simpler wiring
Spindle + laser | 500 W ER11 kit · 10 W 445 nm diode (retail) | Volume-sourced; quotes at 100 units | Where the turnkey case is won or lost
Mask + UV | Syringe LPSM · 10.1" 12K LCD · ChiTu L K1 · 405 nm | Same engine | The LCD also prints jigs in production
Placement jig | Separate Saturn 3 Ultra + wash/cure | Small resin vat + lift under Baker's own UV screen | Removes the printer (to test)
Frame | T-slot extrusion + acrylic | Sheet-metal frame + acrylic panels | Repeatable fabrication
Firmware | Klipper + Moonraker + Proto job runner | Locked factory image; activation stays with us | IP by architecture
Unit cost | ₹3,73,418 (incl. 35% duty/courier, 15% contingency) | ₹1,44,842 (incl. duty, freight, Delhi assembly) | Deck target ₹1,50,000
Sources: PROTOPUS Cost Report (29 Sep 2026, 81 of 96 lines from live listings, USD at ₹88) · workflow story, chapter 6.

## Slide 14
13 · MIXER · AT A GLANCE
Eight instruments, one cable, one brain
2 × scope in · BNC
wavegen out · 2-ch
16 logic lines
DMM leads
2 × supply out
analog front end
AD8066 FET buffers · relay ranges
level shifters
74LVC245 ×2
24-bit multimeter
ADS1256 + REF5025
2 programmable supplies
MCP4728 → XL6009 ×2 · INA226
ADC ×2
AD9226 12-bit 65 MS/s
DAC 2-ch
AN9767 14-bit 125 MS/s
FPGA
Tang Primer 20K
capture + trigger
waveform synthesis
pattern gen
logic sampling
HOST
Raspberry Pi 5
runs Proto
→ Proto compares every reading with what the design expects and writes the verdict in plain words
INSTRUMENT | PROTOTYPE SPEC
Oscilloscope | 2 ch · 12-bit · 65 MS/s
Waveform generator | 2 ch · 14-bit
Logic analyser | 16 ch
Pattern generator | digital stimulus
Protocol decoder | I²C · SPI · serial
Supply 1 + 2 | set-point + current readback
Multimeter | 24-bit
Analog Discovery 3 class. The prototype keeps 12/14-bit converters so the front end can be tuned first.
Status: architecture and BOM defined (₹74,847 prototype); first build in the proof of concept.
Source: workflow story, chapter 4 (signal path drawn from the Mixer BOM).

## Slide 15
14 · MIXER · HOW A TEST RUNS
T1 to T8, in the order a careful engineer would work
T1
Connect
One cable; probes on the test points the design calls for
T2
Power up safely
Supplies set; INA226 watches current, so a bridge is a spike, not a burnt part
T3
Check the rails
24-bit meter reads each rail and reference
T4
Drive the inputs
Generator + pattern generator push known signals
T5
Watch the outputs
Scope for analog, 16-ch logic for digital
T6
Read the buses
Decoder turns captures into I²C/SPI/serial traffic
T7
Verdict
Proto writes what passed, what failed, where to look
T8
Loop
The fix goes into the design; next board the same evening
FUNCTION | PROTOTYPE | PRODUCTION | WHY
Capture | AD9226 12-bit 65 MS/s ×2 | AD9288 dual 8-bit 80 MS/s | cost
Generation | AN9767 dual 14-bit | DAC908 8-bit 165 MS/s ×2 | cost
FPGA | Tang Primer 20K Dock | Tang Nano 9K (GW1NR-9 + 64 Mb PSRAM) | smaller, cheaper
Host | Pi 5 + 7" screen | FT232HL USB 2.0 HS, no screen | one USB cable
Unit cost | ₹74,847 | ₹13,740 | target ₹15,000
ALSO OUR PRODUCTION TESTER
A golden Mixer + our test app tests every Mixer, and every Baker module, on the China line. The factory runs it; we own the limits, software and data.

## Slide 16
15 · TIME PER LOOP, TOLD HONESTLY
About two hours on Baker; 15–20 minutes of it yours
Chart: 
| Load + probe | Mill | Drill | Clean | Mask coat | UV image | Develop + dry | Flood cure | Laser stencil | Paste + release | Place (you) | Reflow + cool | Test on Mixer
low (min) | 5 | 25 | 5 | 2 | 3 | 2 | 4 | 5 | 5 | 3 | 7 | 10 | 5
high (min) | 5 | 45 | 10 | 2 | 5 | 4 | 6 | 10 | 10 | 3 | 14 | 12 | 15
81–141 min
per board, end to end
15–20 min
hands-on: load, place, hook up
 | USUAL LOOP | BAKER + MIXER
Fabrication | outside fab, shipped | steps 01–12, on the bench
Stencil | ordered, aligned by hand | cut in place, same frame
Placement | tweezers or a service | printed jig + vacuum pen
Test | scope, supply, DMM, LA | Mixer: one cable
Diagnosis | engineer reads raw traces | Proto, in plain words
Next attempt | about two weeks later | the same evening
Engineering targets for a 100 × 160 mm board with ~40 parts; the jig prints in parallel. 3–5 boards per 8-hour shift. The proof of concept measures the real numbers.
Notes: Replaces 'send the design at night, pick it up in the morning' (Prateek: too aggressive). You load boards and place parts; we say so and give the minutes.

## Slide 17
16 · A NEW CATEGORY
Between the DIY bench and
industrial manufacturing
DIY bench
breadboards, hand etching, borrowed scopes
protopus
proto + baker + mixer
industrial
fab house, assembly house, bench
TIME PER LOOP
1–3 days
Same day (≈2 h on Baker)
1–3 weeks + customs
EXPERTISE
A seasoned engineer
Proto guides you
Expert to design and test
ASSEMBLED
By hand, if you can
Baker pastes + reflows; you drop parts into a jig
Yes, at extra cost
TESTED
Only if you own a bench
Yes, by Mixer
Separate ₹ lakhs of instruments
BEST FOR
one-off hacks
the first 1–10 boards of a design
100+ identical boards
The DIY bench needs an expert. The factory needs time and money. Most ideas have neither.

## Slide 18
17 · COMPETITION
Others solve one step.
Nobody closes the whole loop.
PRODUCT
PRICE · ₹
MAKE
ASSEMBLE
TEST
GUIDE
Voltera V-One
~3.1 lakh
LPKF ProtoMat
8.6–24.5 lakh
Makera Carvera
~5.1 lakh
Bantam Tools mill · discontinued
~3.1 lakh
Neoden YY1 pick-and-place
<2.6 lakh
Digilent Analog Discovery 3
~33,000
JLCPCB, PCBWay
per order, weeks
Flux (AI design)
1.3–4.3k / month
protopus proto + baker + mixer
3.34 lakh
List prices at ₹88 per US$, before import duty. ASSEMBLE = paste + reflow or placement. Bantam Tools has stopped selling its PCB mill. Flux guides design and stops at the file.
voltera.io · Design World · Makera · ToolGuyd · EEVblog · Digilent · flux.ai
Notes: Column PLACE became ASSEMBLE: we also place parts by hand, into a jig, so the old knock on Voltera no longer holds. Added Carvera, Neoden, Flux and Bantam's exit.

## Slide 19
18 · BUILT FOR PROTOTYPES
Not a desktop mill, not a factory.
Where a fab wins, we say so.
BOARDS A YEAR → RIGHT TOOL
10
baker
same-day loops beat fab minimums
100
baker
one machine covers a busy lab
1,000
2 bakers + a fab
any batch of 10+ identical boards → fab
10,000
fab / EMS
production; Proto exports checked files
1,00,000
fab / EMS
not what Baker is for
One Baker: 3–5 boards per shift, 750–1,250 a year. We scale by the number of labs, not boards per machine.
DESKTOP PCB MACHINES: A ROUGH HISTORY
Othermill → Bantam
PCB mill dropped; now sells art machines
Voltera V-One
out of stock; moved up to NOVA ($45,974)
BotFactory
Squink $3,199–4,499; SV2 now on request
Nano Dimension
sold its electronics unit, Apr 2026, $2M cash
WHY, AND OUR ANSWER
one step automated → the whole loop, mill to verdict
fought $2 boards on price → we sell hours per loop
a tool for experts → an outcome for non-experts
no software → Proto + run data are the moat
Notes: Prateek: don't pitch a desktop PCB mill, and 'will it scale to 1,000 / 10,000 / 1 lakh boards?'. Answer: it's a prototyping cell for iterations 1–10; volume goes to a fab.

## Slide 20
19 · BUSINESS MODEL · PROJECTED
What we aim for: sell the machines, and
one Proto plan runs all of them
PROJECTED PER UNIT · ₹
BAKER
MIXER
Hardware (target)
1,50,000
15,000
Assembly and QC
12,000
2,000
Packing and shipping
8,000
1,000
Warranty reserve
7,500
750
Software share
10,000
2,000
Sales and support
12,500
1,750
Projected total cost
2,00,000
22,500
Target selling price
2,99,000
34,999
Projected margin
~33%
~36%
Costed model: Baker ₹1,44,842, Mixer ₹13,740 incl. assembly.
PLANNED · ONE PROTO PLAN · EVERY MACHINE
₹9,999 / year
One subscription per workspace: Baker Studio, Mixer Station, Proto and every update.
Consumables
Board blanks, mask, paste, film, jig resin and end mills: ≈₹334 of material per board, reordered as labs keep building.
Industrial variants, later
Bigger beds, multilayer and production test come after the base machines.
ROADMAP TO THESE NUMBERS
NOW
Prototypes costed: Baker ₹3.73L, Mixer ₹74,847
MONTHS 0–9 · THIS ASK
₹16L proof of concept: Baker Rev B, 5 Mixers in studios
AFTER POC · SEED
~₹1.5 Cr: China pilots, first 100 Mixers + 20 Bakers
100-UNIT BATCHES
The projected unit economics above

## Slide 21
20 · DOES IT PAY FOR ITSELF?
After about 53 boards, before counting
the two weeks each loop saves
₹334
Baker consumables per board
₹6,721
the same assembled board from JLCPCB, landed in India
53
boards to recover ₹3,33,999 (Baker + Mixer)
COMPARED WITH | SAVING / BOARD | BREAK-EVEN | STARTUP · 2 / WEEK | LAB · 1 / WEEK
JLCPCB → India, 7–20 days | ₹6,387 | 53 boards | 6.6 months | 13.3 months
Indian 24-hour fab, bare boards | ₹5,166 | 65 boards | 8.1 months | 16.3 months
HOW ₹6,721 IS BUILT
5 PCBs $5 · PCBA setup $8 · stencil $1.50 · 200 joints $0.34 · 3 extended parts $9 · DHL $35 → ₹5,178 at ₹88, + 10% BCD and 18% IGST (₹1,543).
WHAT IT LEAVES OUT
Components (you buy them either way), engineer hours and the waiting. The Proto plan, ₹9,999 a year, is worth about two boards.
jlcpcb.com PCB/PCBA pricing · zbotic.in (DHL $25–45, 10% BCD + 18% IGST, 7–20 days door to door; Indian 24-h fab ₹3,000–8,000 for 5) · consumables from the BOM listings.
Notes: Prateek's 'say X lakh, does it cancel my cost?'. At ₹3.34 lakh the pair pays back after ~53 boards against JLCPCB: about 6.6 months for a startup iterating twice a week.

## Slide 22
21 · MARKET PLAN / GROWTH STRATEGY
Start in the maker studios, then
follow the people who watch them
₹6.4L cr
global PCB market
₹3.1L cr
global test and measurement
₹55K cr
India PCB, ~15% a year
₹8.3K cr
India test and measurement
33M+
active Arduino users worldwide
2.3M+
Hackster hardware community
10,000
Atal Tinkering Labs, 50,000 more planned
~2,500
Fab Labs in 125 countries
NOW
Maker studios
Free Baker and Mixer units, with a contract for featured videos. The Bambu Lab playbook.
NEXT
Hobbyists and startups
The people who watch those videos and lose weeks on every board.
ALONGSIDE
Prototyping labs
Tinkering labs, Fab Labs and college labs that already buy tools.
IMARC · Grand View · Arduino · Hackster · Atal Innovation Mission · Forbes · at ₹88 per US$. Bottom-up, India only: 5,868 AICTE colleges × ₹3.34 lakh ≈ ₹196 Cr of hardware.

## Slide 23
22 · CURRENT PROGRESS / ACHIEVEMENTS & TIMELINE
Where we are, told honestly
Baker
Raw prototype running on the bench. The video.
Software
Baker Studio with Proto inside. Website live.
Mixer
Idea phase. Architecture and BOM defined, not built.
SIGNAL
Met Samuel Beek, Founder & CEO of Schematik. Interested in funding us once the proof of concept is ready.
MONTH 0–2
Baker runs all 15 steps on a real board
MONTH 2–4
First Mixer built and measuring
MONTH 4–6
Proof of concept, first maker-studio units
AFTER POC
Next round, first sales

## Slide 24
23 · WHAT THE MONEY PROVES
Our goal: a working proof of concept,
one milestone you can watch at a time
MONTH 2
Baker runs all 15 steps
Blank FR4 to a reflowed board, on video.
MONTH 3
Process proven
PR-001…004: mask, film, jig and laser pass written tests.
MONTH 4
Mixer measures
All 8 instruments checked against reference gear.
MONTH 5
Rev B + Mixer boards
Baker Rev B built; 5 production Mixers pass test.
MONTH 6
Proof of concept
20 boards file-to-tested; Mixers in maker studios.
MONTHS 7–9
Next round
Seed raised on the proof; China quotes out.
₹16 lakh
the whole ask
9 months
6 to proof + 3 to raise
1 + 1
founder + a software engineer who writes firmware
Every month
a demo video + Mixer test logs
Built in the university lab, tested with students and makers.

## Slide 25
24 · WHAT COULD STILL BREAK
Four open points, each written as a pass/fail test
ID | OPEN POINT | TEST ON THE PROTOTYPE | PASS | FALLBACK
PR-001 | Wipe-develop cleanliness, 0.5 mm-pitch pads | 0.5 mm footprint; inspect every pad after step 09 | no mask left on any pad | skim pads with the spindle
PR-002 | Film registration after magnetic clamping | measure film-to-copper offset at fiducials | ±50 µm at every fiducial | clamp sequence / frame stiffness
PR-003 | Jig-to-pin accuracy after resin shrink | post-cure jig; pockets vs pin datum | parts land on pads | scale compensation in the jig
PR-004 | Laser offset drift with temperature | fiducial check, cold start and after a long job | inside the stencil budget | re-check every job (planned)
WHY THE ORDER IS THE DESIGN
mill before mask
the mask covers clean, finished copper
cure before stencil
the laser never touches uncured mask
stencil from the same Gerber, same frame
removes stencil-alignment error
jig prints in parallel
placement adds no waiting
Sn42Bi58 at 138 °C; jig lifts off
stays under TR300's 160 °C; less warp
Also to close before China: one board size, 100 × 160 (workflow) or 100 × 150 mm (BOM blanks). Plus lab safety: Class 4 laser inside an interlocked enclosure.

## Slide 26
25 · GRANT / FUNDING REQUIRED
₹16,00,000
sixteen lakh: nine months to a proof of concept, and time to raise.
₹4.48L
Baker + Mixer builds, costed line by line
₹4,48,265
₹2.20L
Baker Rev B, 5 production Mixers, consumables
₹2,20,000
₹4.50L
One software + firmware engineer, 9 months
₹4,50,000
₹1.35L
Proto software and compute
₹1,35,000
₹1.50L
Testing, tooling, lab safety
₹1,50,000
₹1.97L
IP, outreach, 6.6% reserve
₹1,96,735
Enough to survive one failed iteration and raise from strength.
This builds the proof. The next round, at proof of concept, builds the business.

## Slide 27
26 · COST BREAKUP
Where the ₹16 lakh goes, line by line
Baker
₹3,73,418
Frame & enclosure
22,795
Motion
80,382
Zone A: mill, drill, laser
38,270
Zone B: mask, UV, wipe
33,058
Stencil film
5,805
Placement + reflow
4,891
Board handling
300
Electronics & control
42,985
Resin printer (jigs)
77,698
First-run consumables
6,280
Parts
3,12,465
Import duty + courier
12,247
Contingency (15%)
48,707
Prototype total
₹3,73,418
Mixer
₹74,847
Capture + generation
18,198
Front end + instruments
15,752
Host, screen, I/O
26,752
Enclosure
1,510
Parts
62,212
Import duty + courier
2,872
Contingency (15%)
9,763
Prototype total
₹74,847
PRODUCTION UNIT (PROJECTED)
Baker
₹1,44,842
target ₹1,50,000 · under by ₹5,158
Mixer
₹13,740
target ₹15,000 · under by ₹1,260
Use of funds
₹16,00,000
Baker prototype build
3,73,418
Mixer prototype build
74,847
Baker Rev B iteration
1,00,000
Mixer production board ×5
60,000
PoC consumables
60,000
Engineer (software + firmware)
4,50,000
Proto software + compute
1,35,000
Testing + tooling
1,00,000
Lab set-up + safety
50,000
IP + legal
75,000
Demos + studio outreach
50,000
Reserve (6.6%)
71,735
Total
16,00,000
Hardware ₹4.48L
Iteration ₹2.20L
People ₹4.50L
People 28% · Hardware 28% · Iteration 14% · IP + reserve 12% · Lab + tooling 9% · Software 8%
Basis: PROTOPUS cost report, 29 Sep 2026: 96 BOM lines, 81 from live listings; USD at ₹88; imports carry 35% duty + courier; 15% contingency.

## Slide 28
27 · WHAT'S NEXT
After proof of concept: raise, build in China,
run lean from Delhi
THE ROUND
~₹1.5 crore seed,
at proof of concept
THE CHINA PLAN
Design in Delhi,
build in Shenzhen
OPERATIONS
Delhi finalises,
it doesn't build
China pilots + first batches
₹70L
China set-up, IP
₹25L
Team of 5, 12 months
₹25L
Delhi centre + capital
₹20L
Buffer
₹10L
Seed round
₹1.5 Cr
Pilot batches are sellable (≈₹95L at list). Schematik interested at PoC.
Mixer: full turnkey from batch one.
Baker: China modules, final build in Delhi; turnkey once ≤ $1,305 ex-works.
12 factories quoted → 2 pilots → 1 primary + backup.
Pilots: 20/50/100 Mixers, 3/5/20 Bakers.
Every unit: scan, test, activate Proto, ship.
Mixer is our production tester: our rig, limits, data.
Hire: a mechanical + a manufacturing/quality engineer.
IEC, customs broker, China trademarks first.
MONTH 0–2
Design freeze, 12 RFQs out
MONTH 3–5
Pilots in China: EVT and DVT
MONTH 6–9
PVT: first 100 Mixers, 20 Bakers
MONTH 10–12
Mass production, first container
Months counted from the round. Round sizing is indicative; pilots costed from the BOM.

## Slide 29
28 · CHINA ASSEMBLY LINE · STATION BY STATION
Two kinds of factory, one test system we own
MIXER LINE · FULL TURNKEY EMS, FROM BATCH ONE
M1
IQC
M2
SMT + AOI
M3
THT
M4
program
M5
PCBA FCT
M6
box build
M7
calibrate
M8
8-instr test
M9
serialise
M10
pack
M11
OQC
M12
ship FOB
BAKER LINE · STAGE 1: TESTED MODULES (SKD) IN CHINA, INTEGRATION IN DELHI
B1
IQC
B2
frame
B3
motion
B4
zone A head
B5
zone B head
B6
stencil module
B7
control box
B8
module test (Mixer rig)
B9
kit + crate
D1
Delhi: integrate
D2
Delhi: calibrate
D3
Delhi: make-a-PCB
INDIA FINALISATION CENTRE · NOT A SECOND FACTORY
I1
receive + scan
I2
quarantine
I3
power-on FCT
I4
calibration check
I5
activate Proto licence
I6
accept → stock
WE OWN THE TEST SYSTEM
Golden Mixer + our test app: scan serial → run sequence → PASS/FAIL per step → upload. Operators can't edit limits. One record per serial (PTP-MXR-2027-000173): lots, firmware hash, calibration, every value.
IP BY ARCHITECTURE
The factory flashes a locked image; Proto activation and calibration logic stay with us. NNN in Chinese under PRC law, tooling is ours, no overruns, no substitution without a signed ECN.
Source: PROTOPUS China assembly line master plan (29 Sep 2026), §7, §10, §14, §17.

## Slide 30
29 · CHINA · WHEN TURNKEY WINS
Price the landed cost, not the factory quote
Baker
LINE | TODAY (REPORT) | CHINA TURNKEY
Parts | ₹1,14,547 ($1,302) | inside the ex-works price
Duty | ₹14,775 (16.5%) | 16.5% × EXW (HS to confirm)
Freight | ₹3,520 LCL share | ≈₹8,000 crated machine
India labour | ₹12,000 | ≈₹3,000 acceptance
Landed | ₹1,44,842 | EXW × 1.165 + 11,000
Break-even EXW ≤ $1,305 (≤ $1,356 at the ₹1.5L target) vs $1,302 of parts → start SKD; turnkey when quotes prove it.
Mixer
LINE | TODAY (REPORT) | CHINA TURNKEY
Parts | ₹9,926 ($112.8) | inside the ex-works price
Duty | ₹1,638 | 16.5% × EXW
Freight | ₹176 | ≈₹176 small carton
India labour | ₹2,000 | ≈₹500 acceptance
Landed | ₹13,740 | EXW × 1.165 + 676
Break-even EXW ≤ $127 (≤ $140 at target): $15–27 over parts. Tight at 100, comfortable at 1,000 → turnkey from day one.
NPI GATES · QUANTITIES SIZED TO EACH PRODUCT'S VALUE
GATE | MIXER | BAKER | QUESTION | EXIT (ALL MUST PASS)
EVT | 10 × 2 suppliers | 2–3 module sets each | Can they reproduce it? | meets test spec; Rev B drawings
DVT | 50 | 5 machines | Right for production? | reliability, transport, EMC pre-scan; PR-001…004 on factory units
PVT | 100, sellable | 10–20, sellable | Is the process right? | line operators; yield ≥ target (e.g. 95%); signed authorisation
Source: China assembly line master plan §9 and §12. Freight and India acceptance are the plan's assumptions; duty rate from the cost report. About 12 months to the first container.

## Slide 31
Thank you.
Come and try the loop.
protopus-kappa.vercel.app
soham9763015@ece.du.ac.in
MANAGEMENT TEAM & CORE SKILLS
Who is building this
Soham
Founder
Third year ECE, Faculty of Technology, University of Delhi
Industrial design
Mechanical architecture
Embedded electronics
Machine software
HIRING NEXT · a software engineer who also writes firmware.

## Slide 32
APPENDIX · WHERE THE NUMBERS COME FROM
OUR DOCUMENTS
PROTOPUS Cost Report · BOM workbook · Baker + Mixer workflow (“The story of a PCB”) · China assembly line master plan · all 29 Sep 2026
FAB PRICING
jlcpcb.com PCB and PCBA pages · zbotic.in India shipping, duty and rush-fab guides
MACHINES
voltera.io, eleshop.eu, elektor.com · Design World (LPKF) · Makera (PR Newswire, Jun 2026) · ToolGuyd, Make, Hackaday (Bantam) · TechCrunch (BotFactory) · Evertiq, 8 Apr 2026 (Nano Dimension) · EEVblog (Neoden)
INSTRUMENTS
Digilent AD3 (Jameco, DigiKey) · ADALM2000 (Mouser) · Moku:Go (TEquipment) · Red Pitaya · Saleae
AI
Flux (flux.ai; SiliconANGLE 27 Feb 2026) · Quilter (BusinessWire 7 Oct 2025) · Diode (Fenwick) · claude.com/connectors/autodesk-fusion · digitalproduction.com 30 Apr 2026 (Blender) · Lovable (TechCrunch 23 Jul 2025; founded.com)
MARKET
IMARC · Grand View · Arduino · Hackster · Atal Innovation Mission · Forbes · Fab Foundation · AICTE
CONVENTIONS
USD at ₹88 throughout, to match the cost report. Cycle times are engineering targets until the proof of concept measures them.